Copyright 2014 by The American Institute of Architects (AIA)

Exclusively published and distributed by Architectural Computer Services, Inc. (ARCOM) for the AIA

This Product MasterSpec Section is licensed by ARCOM to Wilsonart LLC ("Licensee").

This Product MasterSpec Section modifies the original MasterSpec text and does not include the full content of the original MasterSpec Section.

Revisions made to the original MasterSpec text are made solely by the Licensee and are not endorsed by, or representative of the opinions of, ARCOM or The American Institute of Architects (AIA). Neither AIA nor ARCOM are liable in any way for such revisions or for the use of this Product MasterSpec Section by any end user. A qualified design professional should review and edit the document to suit project requirements.

For more information, contact Wilsonart LLC, 2501 Wilsonart Dr., Temple, TX 76503-6110; Phone: (254) 207-7000; Toll Free (800) 433-3222; Website: www.wilsonart.com; Sustainable Design Website: http://sustain.wilsonart.com.

For information about MasterSpec, contact ARCOM at (800) 424-5080 or visit www.MasterSpec.com.

SECTION 123661.16 - SOLID SURFACING COUNTERTOPS

TIPS:

To view non-printing Editor's Notes that provide guidance for editing, click on MasterWorks/Single-File Formatting/Toggle/Editor's Notes.

To read detailed research, technical information about products and materials, and coordination checklists, click on MasterWorks/Supporting Information.

Revise this Section by deleting and inserting text to meet Project-specific requirements.

This Section uses the term "Architect." Change this term to match that used to identify the design professional as defined in the General and Supplementary Conditions.

Verify that Section titles referenced in this Section are correct for this Project's Specifications; Section titles may have changed.

GENERAL

RELATED DOCUMENTS

Retain or delete this article in all Sections of Project Manual.

Drawings and general provisions of the Contract, including General and Supplementary Conditions and Division 01 Specification Sections, apply to this Section.

SUMMARY

Section Includes:

Solid surface material countertops.

Solid surface vanities.

Solid surface material backsplashes.

Solid surface material end splashes.

Solid surface material apron fronts.

Solid surface material sinks.

Solid surface walls.

Solid surface window sills.

Solid surface adhesives and sealants.

Related Requirements:

Retain subparagraph below to cross-reference requirements Contractor might expect to find in this Section but are specified in other Sections.

Section 066400 "Plastic Paneling" for plastic paneling.

Section 224100 "Residential Plumbing Fixtures" for [non-integral sinks] [sinks] [and] [plumbing fittings].

ACTION SUBMITTALS

Product Data: For countertop[, wall][, and][ sill] materials[ and sinks] including manufacturer's technical data sheets, and published written instructions.

Sustainable Design Submittals:

"Product Data" Subparagraph below applies to LEED 2009 NC, CI, and CS; LEED v4; IgCC; ASHRAE 189.1; and Green Globes. Coordinate with requirements for adhesives.

Product Data: For adhesives and sealants, indicating VOC content.

"Laboratory Test Reports" Subparagraph below applies to LEED 2009 for Schools, LEED v4, IgCC, ASHRAE 189.1, and Green Globes. Coordinate with requirements for adhesives.

Laboratory Test Reports: For adhesives and sealants, indicating compliance with requirements for low-emitting materials.

Shop Drawings: For countertops. Show materials, finishes, edge and backsplash profiles, methods of joining, terminations, and cutouts.

Show locations and details of joints.

Show direction of directional pattern, if any.

Samples for Initial Selection: For each type of material exposed to view.

Delete "Samples for Initial Selection" Paragraph above if colors and other characteristics are preselected and specified or scheduled. Retain "Samples for Verification" Paragraph below with or without paragraph above.

Samples for Verification: For the following products:

Countertop material, 6 inches (150 mm) square.

Wood trim, 8 inches (200 mm) long.

One full-size solid surface material countertop, with front edge[ and backsplash], 8 by 10 inches (200 by 250 mm), of construction and in configuration specified.

Certificates: For the following certifications:

United States Food and Drug Administration (FDA) compliance for food contact materials described in 21 CFR 174 to 21 CFR 190.

New York City material equipment acceptance, MEA 181-96-M.

ANSI/NSF 51 "food zone" and FDA "direct-food contact" compliant.

UL GREENGUARD® Gold Certified product for low-chemical emissions.

INFORMATIONAL SUBMITTALS

Coordinate "Qualification Data" Paragraph below with qualification requirements in Section 014000 "Quality Requirements" and as may be supplemented in "Quality Assurance" Article.

Qualification Data: For manufacturer and fabricator.

CLOSEOUT SUBMITTALS

Maintenance Data: For solid surface material countertops to include in maintenance manuals. Include Product Data for care products used or recommended by Installer and names, addresses, and telephone numbers of local sources for products.

QUALITY ASSURANCE

Manufacturer Qualifications: ISO 9001 quality management system certification for manufacturing facility(ies).

Retain "Fabricator Qualifications" Paragraph below if required by Project size, fabrication, or installation details.

Fabricator Qualifications: Shop that employs skilled workers who custom-fabricate countertops similar to that required for this Project, and whose products have a record of successful in-service performance.

Manufacturer-certified fabricator.

Installer Qualifications: Manufacturer certified fabricator of countertops.

A mockup may be a reasonable precaution for projects that require many solid surface material countertops, but it may be impractical for other applications.

Mockups: Build mockups to demonstrate aesthetic effects and to set quality standards for fabrication and installation.

Indicate portion of countertop represented by mockup on Drawings or draw mockup as separate element.

Build mockup of typical countertop as [shown on Drawings] [indicated by Architect].

Retain subparagraph below if the intention is to make an exception to the default requirement in Section 014000 "Quality Requirements" for demolishing and removing mockups.

Subject to compliance with requirements, approved mockups may become part of the completed Work if undisturbed at time of Substantial Completion.

FIELD CONDITIONS

Field Measurements: Verify dimensions of countertops by field measurements[ after base cabinets are installed but] before countertop fabrication is complete.

COORDINATION

Coordinate locations of utilities that will penetrate countertops or backsplashes.

WARRANTY

When warranties are required, verify with Owner's counsel that warranties stated in this article are not less than remedies available to Owner under prevailing local laws.

Manufacturer's Warranty: Manufacturer and installer agree to repair or replace sheet material not free from defects in materials, fabrication, or workmanship within specified warranty period.

Warranty applies only to the Wilsonart Solid Surface sheet product that has been fabricated and permanently installed by a Certified Wilsonart® Fabricator in an interior commercial or residential application in the United States or Canada, and remains at that location.

Warranty Period: 10 years from date of Substantial Completion.

PRODUCTS

Manufacturers and products listed in SpecAgent and MasterWorks Paragraph Builder are neither recommended nor endorsed by the AIA or ARCOM. Before inserting names, verify that manufacturers and products listed there comply with requirements retained or revised in descriptions and are both available and suitable for the intended applications. For definitions of terms and requirements for Contractor's product selection, see Section 016000 "Product Requirements."

"Wilsonart® Solid Surface" is manufactured with acrylic resins, fire-retardant fillers, and proprietary coloring agents that are homogeneous, with uniform color throughout their thickness. "Wilsonart® Solid Surface" is designed for interior use only. Refer to the "Wilsonart® Solid Surface" fabrication manual or contact a Certified "Wilsonart® Solid Surface" Fabricator for details. Final finish is completed by the fabricator and may range from matte to high gloss, depending on the customer's specification. Surfaces with gloss and semi-gloss finishes require more maintenance than matte or satin finishes. Darker colors will require special attention.

SOLID SURFACE COUNTERTOP AND WALL MATERIALS

Composition Solid-Surface Material: Homogeneous-filled plastic resin complying with ICPA SS-1.

          - Basis-of-Design Product: Subject to compliance with requirements, provide Wilsonart LLC; [051] [025] or a comparable product by one of the following:

Affinity Surfaces; a brand of Domain Industries, Inc.

Avonite Surfaces.

E. I. du Pont de Nemours and Company.

Formica Corporation.

LG Chemical, Ltd.

Meganite Inc.

Samsung Chemical USA, Inc.

Swan Corporation (The).

Transolid Div of Trumbull Industries.

<Insert manufacturer's name>.

Retain first option in "Thickness" Subparagraph below for Wilsonart's "Product Type 051," and second option for Wilsonart's "Product Type 025."

Thickness: [0.490 inch (12.4 mm)] [0.240 inch (6.1 mm)].

Retain first option in "Panel Weight" Subparagraph below for Wilsonart's "Product Type 051," and second option for Wilsonart's "Product Type 025."

Panel Weight: [4.4 lb/sq. ft. (21.5 kg/sq. m)] [2.2 lb/sq. ft. (10.7 kg/sq. m)].

Surface-Burning Characteristics: Comply with ASTM E 84; testing by a qualified testing agency. Identify products with appropriate markings of applicable testing agency.

Flame-Spread Index: [25] <Insert value> or less.

Smoke-Developed Index: [50] [450] <Insert value> or less.

Integral Sink Bowls: Comply with CSA B45.5/IAPMO Z124.

For color and pattern information, see www.wilsonart.com/solid-surface/design-library.

Colors and Patterns: [As indicated by manufacturer's designations] [Match Architect's samples] [As selected by Architect from manufacturer's full range].

Retain "Solid Wood Edges and Trim" Paragraph below for countertops with decorative wood edge. Wood species are examples only; other species may be available. Indicate details on Drawings.

Solid Wood Edges and Trim: Clear [red oak] [white oak] [hard maple] [cherry] <Insert species> lumber, free of defects, selected for compatible grain and color, and kiln dried to 7 percent moisture content.

"Certified Wood" Subparagraph below applies to LEED v4. Manufacturers certifying products as "FSC Mixed Credit" do not have to use 100 percent certified wood in the products; however, in their total production, manufacturers must use an amount equal to or greater than the percentage of their production that is labeled "FSC Mixed Credit."

Certified Wood: Wood products shall be certified as "FSC Pure"[ or "FSC Mixed Credit"] according to FSC STD-01-001 and FSC STD-40-004.

"Composite Wood Products" Paragraph below applies to LEED v4.

Composite Wood Products: Products shall be made using ultra-low-emitting formaldehyde resins as defined in the California Air Resources Board's "Airborne Toxic Control Measure to Reduce Formaldehyde Emissions from Composite Wood Products" or shall be made with no added formaldehyde.

Retain "Particleboard" or "Plywood" Paragraph below if 1/4-inch- (6.4-mm-) thick, solid surface material is specified or if subtops are required.

Particleboard: ANSI A208.1, [Grade M-2] [Grade M-2-Exterior Glue].

Plywood: Exterior softwood plywood complying with DOC PS 1, Grade C-C Plugged, touch sanded.

COUNTERTOP FABRICATION

Fabricate countertops according to solid surface material manufacturer's written instructions and to the AWI/AWMAC/WI's "Architectural Woodwork Standards."

Grade: [Premium] [Custom] [Economy].

Delete "Configuration" Paragraph below if countertop is indicated on Drawings.

Configuration:

Retain one front and one backsplash style in first two subparagraphs below or revise to suit Project.

Front: [Straight, slightly eased at top] [Beveled] [3/4-inch (19-mm) bullnose] [Radius edge with apron, 2 inches (50 mm) high with 3/8-inch (9.5-mm) radius] [1-1/2-inch (38-mm) bullnose] [1-inch (25-mm) bullnose] [Straight, slightly eased at top with separate apron, 6 inches (150 mm) high, recessed 1/4-inch (6.4-mm) behind front edge].

Backsplash: [Straight, slightly eased at corner] [Beveled] [Radius edge with 3/8-inch (9.5-mm) radius].

End Splash: [Matching backsplash] [None].

Retain one of two "Countertops" paragraphs below and revise to suit Project. Availability of 3/4-inch- (19-mm-) thick, solid surface material is limited.

Countertops: 1/2-inch (12.7-mm) thick, solid surface material with front edge built up with same material.

Countertops: 1/4-inch (6.4-mm) thick, solid surface material laminated to 3/4-inch (19-mm) thick particleboard with [wood-trimmed exposed edges] [exposed edges built up with 3/4-inch (19-mm) thick, solid surface material] [exposed edges faced with 1/4-inch (6.4-mm) thick, solid surface material].

Backsplashes: [1/2-inch (12.7-mm)] [3/4-inch (19-mm)] thick, solid surface material[ with wood-trimmed edges].

Fabricate tops with shop-applied edges[ and backsplashes] unless otherwise indicated. Comply with solid surface material manufacturer's written instructions for adhesives, sealers, fabrication, and finishing.

Delete option in last paragraph above or delete first subparagraph below; delete both for Contractor's option.

Fabricate with loose backsplashes for field assembly.

Delete subparagraph below if no integral sinks.

Install integral sink bowls in countertops in the shop.

Retain one of two "Joints" paragraphs below. First paragraph is impossible with very large or complex countertops. If retaining second paragraph and option, indicate joint locations on Drawings.

Joints: Fabricate countertops without joints.

Joints: Fabricate countertops in sections for joining in field[, with joints at locations indicated].

Consider retaining "Joint Locations" Subparagraph below if joint locations are not indicated on Drawings.

Joint Locations: Not within 3 inches (76 mm) of a cutout or cooktop, 1 inch (25 mm) from inside corner for conventional seams, and not where countertop sections less than 36 inches (900 mm) long would result, unless unavoidable.

Cutouts and Holes:

Retain "Undercounter Plumbing Fixtures" Subparagraph below for undercounter lavatories and sinks. Shop fabrication usually provides better results, but large openings, such as for kitchen sinks, are better completed after top is in place to avoid possibility of breakage during delivery or installation.

Undercounter Plumbing Fixtures: Make cutouts for fixtures[ in shop] using template or pattern furnished by fixture manufacturer. Form cutouts to smooth, even curves.

Retain one of first three subparagraphs below to describe profile of cutout edges or indicate on Drawings.

Provide vertical edges, slightly eased at juncture of cutout edges with top and bottom surfaces of countertop.

Provide vertical edges, rounded to 3/8-inch (10-mm) radius at juncture of cutout edges with top surface of countertop, slightly eased at bottom.

Retain "Counter-Mounted Plumbing Fixtures" Subparagraph below for counter-mounted lavatories, sinks, and so forth. Shop fabrication usually provides better results, but large openings, such as for kitchen sinks, are better completed after top is in place to avoid possibility of breakage during delivery or installation.

Counter-Mounted Plumbing Fixtures: Prepare countertops in shop for field cutting openings for counter-mounted fixtures. Mark tops for cutouts and drill holes at corners of cutout locations. Make corner holes of largest radius practical.

Retain "Fittings" Subparagraph below if using deck-mounted fittings or soap dispensers.

Fittings: Drill countertops in shop for plumbing fittings, undercounter soap dispensers, and similar items.

Counter-Mounted Cooktops: Prepare countertops in shop for field cutting openings for cooktops. Mark tops for cutouts and drill holes at corners of cutout locations. Make corner holes of largest radius practical.

INSTALLATION MATERIALS

Adhesive: Product recommended by solid surface material manufacturer.

Subparagraph below applies to LEED 2009 NC, CI, and CS; LEED v4; IgCC; ASHRAE 189.1; and Green Globes. VOC content limit is that for multipurpose construction adhesives.

Adhesives shall have a VOC content of [70] <Insert value> g/L or less.

Subparagraph below applies to LEED v4.

Adhesive shall comply with the testing and product requirements of the California Department of Public Health's "Standard Method for the Testing and Evaluation of Volatile Organic Chemical Emissions from Indoor Sources Using Environmental Chambers."

Sealant may be required for joints at walls. If retaining "Sealant for Countertops" Paragraph below, coordinate with Section 079200 "Joint Sealants."

Sealant for Countertops: Comply with applicable requirements in Section 079200 "Joint Sealants."

EXECUTION

EXAMINATION

Coordinate conditions required by Work of this Section with requirements in other Sections in which substrates are specified.

Examine substrates to receive solid surface material countertops and conditions under which countertops will be installed, with Installer present, for compliance with requirements for installation tolerances and other conditions affecting performance of countertops.

Proceed with installation only after unsatisfactory conditions have been corrected.

INSTALLATION

Install countertops level to a tolerance of 1/8 inch in 8 feet (3 mm in 2.4 m), 1/4 inch (6 mm) maximum. Do not exceed 1/64-inch (0.4-mm) difference between planes of adjacent units.

Retain first paragraph below if solid surface countertop is fastened directly to cabinets or other supports.

Fasten countertops by adhering with 100-percent silicone material in dab format (not bead format) to base units into underside of countertop at 18 to 24 inches (457 to 610 mm) o.c. Align adjacent surfaces and, using adhesive in color to match countertop, form seams to comply with manufacturer's written instructions. Carefully dress joints smooth, remove surface scratches, and clean entire surface.

Retain first two paragraphs below if solid surface countertop is installed over a plywood or particleboard subtop.

Fasten countertops by adhering with 100-percent silicone material in dab format (not bead format) to base units into underside of countertop at 18 to 24 inches (457 to 610 mm) o.c. Shim as needed to align subtops in a level plane.

Secure countertops to subtops or wood-web frame with adhesive according to solid surface material manufacturer's written instructions. Align adjacent surfaces and, using adhesive in color to match countertop, form seams to comply with manufacturer's written instructions. Carefully dress joints smooth, remove surface scratches, and clean entire surface.

Retain first paragraph below unless joints are not allowed.

Bond joints with adhesive and draw tight as countertops are set. Mask areas of countertops adjacent to joints to prevent adhesive smears.

Clamp units to temporary bracing, supports, or each other to ensure that countertops are properly aligned and joints are of specified width.

Install backsplashes and end splashes by adhering to wall and countertops with adhesive. Mask areas of countertops and splashes adjacent to joints to prevent adhesive smears.

Complete cutouts not finished in shop. Mask areas of countertops adjacent to cutouts to prevent damage while cutting. Make cutouts to accurately fit items to be installed, and at right angles to finished surfaces unless beveling is required for clearance. Ease edges slightly to prevent snipping.

Apply sealant to gaps at walls; comply with Section 079200 "Joint Sealants."

END OF SECTION 123661.16